## Slide 1
This gets turned 90 counterclockwise so note A0 (MIDI note 21)
is at the left and C8 (MIDI 108) is at the right of the image, just like the piano.
Edge of paper
Edge of paper
286mm
252.2 mm
A0
21
C8
108
18.6 mm
1.44 mm (all notes have equal width)
1.44 mm (all spaces have equal width)
11
mm
Loud
Pedal
1.55
mm
15.2 mm
30 seconds
=
1070 mm
@ Tempo 70
Paper moves down when playing
Note Space
Long notes ( more than 17 mm long on the roll or roughly 1/2 second long) need to be cut differently to prevent tears.
An initial section of roughly 8 5 mm with subsequent 1.52 4mm squares with 0.8mm spaces between them with a final opening of 8 5 mm to close the note. This way the vacuum stays broken through the whole length and prevent the two side from tearing apart.
Converting MIDI file information into vector file for plotter/cutter production of piano roll – Version 1.2
Cut openings on piano roll
245.9 mm
21.5 mm
1.37 mm

## Slide 3
21
24
36
48
60
72
94
98
To 108
53
58
62
70